## Slide 1: Computer Networks
Routing protocols

## Slide 2: Routing protocols

## Slide 3: The matrices by routing protocols

## Slide 4: The matrices by routing protocols
Routing protocols store the result of these matrices in routing tables:
Bandwidth:
  Maximum data transfer rate across a network path
Delay:
  Time it takes for data packets to travel from a source to a destination through various network nodes
Load:
  Refers to the level of traffic or demand on network resources
MTO:
  Refers to minimizing the additional data or processing required to direct information packets efficiently from one point to another, to enhance network performance.

## Slide 22: Area Border Router
A router that has OSPF neighbor relationships with devices in multiple OSPF areas. ABRs gather topology information from their connected areas and distribute it to the backbone area.

## Slide 23: Autonomous System Boundary Router (ASBR)
ASBR is a router that attaches to more than one routing protocol and exchanges routing information between them.

## Slide 24: Internal Router
A router that has OSPF neighbor relationships only with devices in the same area.

## Slide 25: Backbone Router
A backbone router is a router that runs OSPF and has at least one interface connected to the OSPF backbone area.