## Slide 1
Miss Rabia Qasim
Computer Network

## Slide 2: Distribution

## Slide 3: Books
Computer Networking, A Top-Down Approach by James F. Kurose
Reference books:
Computer Networking Problems and Solutions & quot; by Russ White and Ethan
Banks
 Network Fundamentals CCNA Exploration Companion Guide, Mark Dye.
 Behrouz A. Forouzan, Data Communications and Networking, Mc-Graw.
 Computer Networks, A system approach, Larry Peterson &amp; Bruce Davie.

## Slide 4: Network
A network is a collection of computers and devices connected together via transmission medium or channel for the sharing of the data.
Connections between computing devices can be physical using wires or wireless
Advantages of a network include:
Facilitating
communications
Sharing
hardware
Sharing data
and information
Sharing
software

## Slide 5: Network
Node (host)
  Any device on a network
Bandwidth
  Bandwidth describes the maximum data transfer rate of a network or Internet connection. It measures how much data can be sent over a specific connection in a given amount of time.
  For example, a gigabit Ethernet connection has a bandwidth of 1,000 Mbps

## Slide 6: Network
Packets
  Pieces of data transmitted over a network
    Packets are created by sending node
    Data is reassembled by receiving node
  Packet header
    Sending and receiving address

## Slide 7: Types of Networks
Local-area network (LAN)
  A local area network (LAN) is a network that connects computers and devices in a limited geographical area such as a single building or a college campus
  A wireless LAN (WLAN) is a LAN that uses no physical wires

## Slide 8: Types of Networks
Local Area Network (LAN)
  Systems are close to each other
  Contains printers, servers and computers
  Organizations often have several LANS
  It is usually a privately owned network
  LAN’s are easy to design and troubleshoot

## Slide 9: Types of Networks
Wide Area Networks (WAN)
  A wide area network (WAN) is a network that connects computers and devices over a large geographic area
  The Internet is a WAN

## Slide 10: Types of Networks
Wide Area Networks (WAN)
  Two or more LANs connected
  Over a large geographic area
  Computers are at widely separated locations

## Slide 11: Types of Networks
Metropolitan Area Network (MAN)
  It is in between LAN & WAN technology that covers the entire city.
  Large network that connects different organizations
Home Area Network (HAN)
  Small scale network
  Connects computers and entertainment appliances
  Found mainly in the home

## Slide 12: Types of Networks
Personal Area Network (PAN)
  A personal area network is a computer network organized around an individual person
  Very small scale network
  Range is less than 2 meters
  Cell phones, MP3 players

## Slide 13: Network Topologies
Topology
  A network topology is the pattern in which nodes are connected to a local area network (LAN) or other network
  Choice affects
    Network performance
    Network size
  Several different types
    Bus Topology: Single central cable connected a number of devices
    Star Topology: Connecting all devices to a central unit
    Ring Topology: A number of computers are connected on a closed loop
    Mesh Topology: Each device is connected to every other device in the network

## Slide 14: Types of Networks

## Slide 15: Network Topologies
Bus topology
  One main cable to which all nodes are directly connected
  The main cable acts as a backbone for the network
  Advantages
    Easy and cheap
    Small amount of wire
  Disadvantages
    If the main cable breaks, the entire network goes down

## Slide 16: Network Topologies
Star topology
  Each computer has a cable connected to a single point
  All nodes connect to a hub:
    All data must pass through the hub
    Hub sends packet to destination
  Advantages
    Easy to setup
    One cable can not crash network
  Disadvantages
    If hub goes down, entire network down
    Uses lots of cable

## Slide 17: Network Topologies
Ring topology
  Nodes connected in a circle
    Data travels in one direction
  Tokens used to transmit data
    Only the computer who gets the token can send data
  Advantages
    Reduced chances of data collision as each node release a data packet after receiving the token
  Disadvantages
    The entire network will be effected if one workstation shuts down

## Slide 18: Network Topologies
Advantages of Mesh topology
  All computers connected together
  Internet is a mesh network
    Data will always be delivered
  Disadvantages
    Lots of cable
    Hard to setup

## Slide 19: Network Hardware
Network interface cards
  Network adapter
  Connects node to the media
  Unique Machine Access Control (MAC) Address

## Slide 20: Network Hardware
Hubs
  A device that is used to connect several computers to form a network
  A hub has several ports. The number generally is 8, 12, 16, 24,
32, or 48
  Center of a star network
  All nodes receive transmitted packets
  Slow and insecure
Switches
  Replacement for hubs
  Only particular node receives transmission
  Fast and secure
      Both: Hubs broadcast data to all devices, switches forward data based on MAC addresses

## Slide 21: Network Hardware
A hub or switch connects several devices in a network together

## Slide 22: Network Hardware
Router
  A router is a device that forwards data packets along networks.
  Routers connect different networks and route data packets between them based on IP addresses.

## Slide 23: Types of communication
According to data direction
  Simplex
    One-way communication (only send or only receive)
  Half-Duplex
    Two-way communication (send/receive) but one at a time
  Full Duplex
    Two-way communication (send/receive) at the same time

## Slide 24: Types of communication
According to recipients
  Unicast
    Sending data to only one recipient
  Multicast
    Sending data to multiple recipients
  Broadcast
    Sending data to everybody

## Slide 25: Gateway
A gateway is a networking device that connects two dissimilar networks, translating protocols to facilitate communication, typically serving as an entry and exit point for data between networks.
14