## Slide 1
Network Architecture, Protocol, and Transmission Media

## Slide 2: Introduction to Computer Networks
Network Architecture
Network Protocols
Network Channels (Media)
Physical Transmission Media
Wireless Transmission Media
Wireless Transmission Devices

## Slide 3: Network Architecture
Refers to how the computer or devices are designed in a network
Basic types:
  Client/Server:
    All clients must request service from the server
    The server is also called a host
    Node is any network device
    Nodes are called clients

## Slide 4: Network Architecture
Client/Server Network
  Servers are used to control access
  Users gain access by logging in
  Database software
    Access to data controlled by server
  Server is the most important computer
  Different servers perform different tasks: File server, network server, etc.
    A file server specifically manages and shares files within a network, while a network server encompasses a broader range of services beyond file storage, such as email, web hosting, and database management.

## Slide 5: Network Architecture
Peer to Peer Networks (P2PN)
  All nodes are equal
  Nodes access resources on other nodes
  Each node controls its own resources
  Most modern OS allow P2PN
  Good for small businesses and home networks
  Simple and inexpensive

## Slide 6: Network Protocols
Protocol
  A set of rules that defines how data is formatted and processed on a network
  Integration of three basic functions:
    What is communicated?
    How is it communicated?
    When is it communicated?
  Language of the network
    Rules of communication
    Error control
    Size of packet

## Slide 7: Network Protocols
Hypertext Transfer Protocol (HTTP): A client/server application that uses TCP for transport to retrieve HTML pages.
Domain Name Service (DNS): A name-to-address translation application that uses both TCP and UDP transport.
File Transport Protocol (FTP): A file transfer application that uses TCP for transport.
Network Time Protocol (NTP): An application that synchronizes time with a time source and uses UDP for transport.
    Synchronize the clocks of computers and other network devices over a network, ensuring accurate timekeeping for activities such as logging and authentication.

## Slide 8: Network Channels (Media)
A channel is a path between two communication devices
Channel capacity: How much data can be passed through the channel (bit/sec)
  Also called channel bandwidth
Consists of one or more transmission media
  Two types:
    Physical: wire cable
    Wireless: Air

## Slide 9: Physical Transmission Media
Twisted-pair cabling (Ethernet Cable)
  Most common LAN cable
  Called Cat5, Cat6
  Four pairs of copper cable twisted
  Speeds range from 1 Mbps to 1,000 Mbps

## Slide 10: Physical Transmission Media
Coaxial cable
  Similar to cable TV wire
  central conductor surrounded by insulation
  Speeds up to 10 Mbps

## Slide 11: Physical Transmission Media
Fiber-optic cable
  Data is transmitted with light pulses
  Glass strand instead of cable
  Speeds up to 100 Gbps

## Slide 12: Wireless Transmission Media
Broadcast Radio
  Medium that distributes radio signals through the air.
  Uses an antenna, can be short range
  Bluetooth is a kind of short-range (about 10 meters) broadcast radio communications
Cellular Radio
  A form of broadcast radio used for mobile communication
  High frequency radio waves to transmit voice or data
      Difference: Broadcast radio sends content over a wide area for anyone to receive, while cellular radio enables mobile communication through a network of cells, managing individual connections dynamically.

## Slide 13: Wireless Transmission Media
Microwaves
  Radio waves providing high speed transmission
  Microwaves must transmit in a straight line with no barrier between microwave antennas
  Used for satellite communication
Infrared (IR)
  Wireless transmission media that sends signals using infrared light-waves
  IR transmission also requires a line-of-sight transmission as that required by microwaves
  Infrared waves have shorter wavelengths and lower frequencies than radio waves.

## Slide 14: Wireless Transmission Devices
Wireless Access Point
  Center of a wireless network
  WAPs combined cover a larger area
  Range is 50 to 150 meters

## Slide 15: Wireless Transmission Devices
Wireless Adapters
  Wireless adapters are hardware devices that enable computers to connect to wireless networks by transmitting and receiving wireless signals.