## Slide 1: Inter-VLAN Routing

## Slide 2: What is inter-VLAN
VLANs are used to segment switched Layer 2 networks for a variety of reasons. Regardless of the reason, hosts in one VLAN cannot communicate with hosts in another VLAN unless there is a router or a Layer 3 switch to provide routing services.
Inter-VLAN routing is the process of forwarding network traffic from one VLAN to another VLAN.
There are three Inter-VLAN routing options:
  Legacy Inter-VLAN routing: This is a legacy solution. It does not scale well.
  Router-on-a-Stick: This is an acceptable solution for a small- to medium-sized network.
  Layer 3 switch using switched virtual interfaces (SVIs): This is the most scalable solution for medium to large organizations.

## Slide 3: Legacy Inter-VLAN routing
The first inter-VLAN routing solution relied on using a router with multiple Ethernet interfaces. Each router interface was connected to a switch port in different VLANs. The router interfaces served as the default gateways to the local hosts on the VLAN subnet.

## Slide 4: Legacy Inter-VLAN routing: Pros and Cons
Advantages
Simple to implement
Cost-effective
Suitable for small networks
Works well with older hardware
No need for additional equipment
Disadvantages
Limited scalability
Increased broadcast traffic
Lack of granular control
Security concerns
Performance degradation

## Slide 5: Router-on-a-Stick
The “router-on-a-stick” inter-VLAN routing method overcomes the limitation of the legacy inter-VLAN routing method. It requires only one physical Ethernet interface to route traffic between multiple VLANs on a network.
A Cisco IOS router Ethernet interface is configured as an 802.1Q trunk and connected to a trunk port on a Layer 2 switch. Specifically, the router interface is configured using sub-interfaces to identify routable VLANs.
Notes: 802.1Q trunk: The 802.1Q trunk is a networking technology used to carry multiple VLANs over a single physical link between network devices, typically switches. It's a standardized protocol defined by the IEEE 802.1Q standard.

## Slide 6: Router-on-a-Stick: Pros and Cons
Advantages
Scalability
Performance
Control
Flexibility
Features
Disadvantages
Complexity
Single Point of Failure
Cost
Requirements
Additional Equipment

## Slide 7: Layer 3 switch
The modern method of performing inter-VLAN routing is to use Layer 3 switches and switched virtual interfaces (SVI). An SVI is a virtual interface that is configured on a Layer 3 switch.
Inter-VLAN SVIs are created the same way that the management VLAN interface is configured.
The SVI is created for a VLAN that exists on the switch. Although virtual, the SVI performs the same functions for the VLAN as a router interface would.
Specifically, it provides Layer 3 processing for packets that are sent to or from all switch ports associated with that VLAN.
Notes: 802.1Q trunk: The 802.1Q trunk is a networking technology used to carry multiple VLANs over a single physical link between network devices, typically switches. It's a standardized protocol defined by the IEEE 802.1Q standard.

## Slide 8: Layer 3 switch: Pros and Cons
Advantages
Performance
Scalability
Efficiency
Control
Flexibility
Disadvantages
Cost
Complexity
Limited Routing Features
Hardware Requirements
Single Point of Failure